## Slide 1
4.5 Code Division Multiple Access ( CDMA)
CDMA is another pure digital technique. Where the analog speech is coded into digital signals. Each conversation is assigned a unique code (a signature for each individual transmission). The codes of different users are assigned to be different from each other . The final signal at the receiver contains only the relevant conversation. Any other signals are picked up as a noise.
Fig 4.9

## Slide 2
CDMA is also known as spread spectrum , because it takes the digitized version of an analog signal and spreads it out over a wider bandwidth at a lower power level. This method is called direct sequence spread spectrum (DSSS) as well (Fig. 4.11 ). The digitized and compressed voice signal in serial data form is spread by processing it in an XOR circuit along with a chipping signal at a much higher frequency.
Fig 4.11

## Slide 3
4.5.1 Introduction to Spread Spectrum Communications
CDMA is a form of Direct Sequence Spread Spectrum communications. In general, Spread Spectrum communications is distinguished by three key elements:
1. The signal occupies a bandwidth much greater than that which is necessary to send the information. This results in many benefits, such as immunity to interference and jamming and multi-user access .
2. The bandwidth is spread by means of a code which is independent of the data. The independence of the code distinguishes this from standard modulation schemes in which the data modulation will always spread the spectrum somewhat.

## Slide 4
3. The receiver synchronizes to the code to recover the data. The use of an independent code and synchronous reception allows multiple users to access the same frequency band at the same time.
In order to protect the signal, the code used is pseudo-random. It appears random, but is actually deterministic, so that the receiver can reconstruct the code for synchronous detection. This pseudo-random code is also called pseudo-noise (PN).

## Slide 5
There are three ways to spread the bandwidth of the signal:
Frequency hopping.
Time hopping.
Direct sequence.
4.5.2 Direct Sequence Spread Spectrum
CDMA is a Direct Sequence Spread Spectrum system. The CDMA system works directly on 64 kbit/sec digital signals. These signals can be digitized voice, ISDN channels, modem data, etc.
Figure 5.12 shows a simplified Direct Sequence Spread Spectrum system. For clarity, the figure shows one channel operating in one direction only.
Signal transmission consists of the following steps:

## Slide 6
1. A pseudo-random code is generated, different for each channel and each successive connection.
2. The Information data modulates the pseudo-random code (the Information data is “spread”).
3. The resulting signal modulates a carrier.
4. The modulated carrier is amplified and broadcast.
Figure 4.12 Spreading operation spreads the signal energy over a wider frequency bandwidth.

## Slide 7
Only the desired signal, which has the key, will be seen at the receiver when the despreading operation is exercised. See Figure 4.13.
Figure 4.13. A spread-spectrum communication system. Note that the interferer's energy is spread while the data signal is despread in the receive chain.

## Slide 8
Signal reception consists of the following steps:
1. The carrier is received and amplified.
2. The received signal is mixed with a local carrier to recover the spread digital signal.
3. A pseudo-random code is generated, matching the anticipated signal.
4. The receiver acquires the received code and phase locks its own code to it.
5. The received signal is correlated with the generated code, extracting the Information data.
4.5.3 Generating Pseudo-Random Codes
For each channel the base station generates a unique code that changes for every connection. The base station adds together all the coded transmissions for every subscriber. The subscriber unit correctly generates its own matching code and uses it to extract the appropriate signals. Note that each subscriber uses several independent channels.

## Slide 9
Data for transmission is combined via bitwise XOR (exclusive OR) with the faster code. The figure shows how spread spectrum signal is generated. The data signal with pulse duration of Tb is XOR’ed with the code signal with pulse duration of Tc. (Note: bandwidth is proportional to 1 / T where T = bit time) Therefore, the bandwidth of the data signal is 1 / Tb and the bandwidth of the spread spectrum signal is 1 / Tc. Since Tc is much smaller than Tb, the bandwidth of the spread spectrum signal is much larger than the bandwidth of the original signal. The ratio Tb / Tc is called spreading factor or processing gain and determines to a certain extent the upper limit of the total number of users supported simultaneously by a base station .

## Slide 10
Figure 4.14. Pseudo-Noise Spreading

## Slide 11
Figure 4.15 shows the process of frequency spreading. In general, the bandwidth of a digital signal is twice its bit rate. The bandwidths of the information data (fi) and the PN code are shown together. The bandwidth of the combination of the two, for fc>fi, can be approximated by the bandwidth of the PN code
Figure 4.15. Frequency Spreading

## Slide 12
Spread spectrum (SS) is a means of transmission in which:
1. The transmitted signal occupies a bandwidth which is much greater than the
minimum necessary to send the information.
2. Spreading is accomplished by means of a spreading signal called a ‘code’ signal,
which is independent of the data.
3. At the receiver, dispreading is done by correlating the received SS signal with a
Synchronized replica of the spreading signal.

## Slide 13
A narrowband signal is spread to a wideband signal (example: CDMA):
C = B Log2 (1+ S/N)
C is the channel capacity in bits per second (bps), which is the maximum data rate for a theoretical bit-error rate (BER).
• B is the required channel bandwidth in Hz,
• S/N is the signal-to-noise power ratio.
=> Very roughly, C/B = S/N , which means:
To send error-free information for a given signal-to-noise ratio in the channel, therefore, we need only perform the fundamental SS signal-spreading operation: increase the transmitted bandwidth.

## Slide 15
4.5.4 Processing Gain
An important concept relating to the bandwidth is the processing gain (Gp). This is a theoretical system gain that reflects the relative advantage that frequency spreading provides. The processing gain is equal to the ratio of the chipping frequency to the data frequency :
=
Chipping Frequency (fc): the bit rate of the PN code.
Information rate (fi): the bit rate of the digital data.
The higher the processing gain, the greater the DSSS signal’s ability to fight interference.

## Slide 16
Example:
If a 1 KHz signal is spread to 100 KHz, the process gain expressed as a numerical ratio would be 100,000/1,000 = 100. Or in decibels,
10log10 (100) = 20 dB.
A 13kbps binary signal is spread over a bandwidth of 1.25 MHz using BPSK. What is the processing gain of the resulting DSSS signal? Express the answer as a ratio and in decibels.
There are two major benefits from high processing gain:
Interference rejection: the ability of the system to reject interference is directly proportional to Gp.
System capacity: the capacity of the system is directly proportional to Gp.

## Slide 17
So the higher the PN code bit rate (the wider the CDMA bandwidth), the better the system performance.
4.5.4 Code Correlation
In this context, correlation has a specific mathematical meaning. In general the correlation function has these properties:
It equals 1 if the two codes are identical
It equals 0 of the two codes have nothing in common
Intermediate values indicate how much the codes have in common. The more they have in common, the harder it is for the receiver to extract the appropriate signal.
There are two correlation functions:
Cross-Correlation: The correlation of two different codes. As we’ve said, this should be as small as possible.
Auto-Correlation: The correlation of a code with a time-delayed version of itself. In order to reject multi-path interference, this function should equal 0 for any time delay other than zero.

## Slide 18
The receiver uses cross-correlation to separate the appropriate signal from signals meant for other receivers, and auto-correlation to reject multi-path interference.
4.5.5 CDMA Codes
CDMA Standard uses three types of codes namely 1) Long code 2) Short code and 3) Walsh codes .
a. Walsh codes: - it is use to differentiate the channels in downlink (forward link). It is used to communicate from BS to Mobile.
This provides orthogonal encoding is that characterized by the following property when they are multiplexed:
• If they were encoded with the same code, the result is acknowledged by the receiving system.
• If they were encoded with different codes, the result is ignored by the receiving system.

## Slide 19
b. Long code: - it is use to differentiate the channels in uplink (reverse link). It is used to communicate from mobile to BS. The long code is used to encrypt the content of the transmitted signal, and thus ensures privacy.
c. Short code: - this code is used to identify to the mobile, the antenna face, and the base station that the mobile is communicating with. This is also PN code.