## Slide 1
Chapter 4
Multiple access techniques for wireless system
4.1 Introduction;
Multiple access schemes are used to allow many mobile users to share
simultaneously a finite amount of radio spectrum. The sharing of spectrum is required to achieve high capacity by simultaneously allocating the available bandwidth (or the available amount of channels) to multiple users. For high quality communications, this must be done without severe degradation in the performance of the system.
The techniques used to access a satellite, so that the frequency spectrum and power are shared efficiently between a large number of users. A multiple access scheme must be able to optimize the following parameters:

## Slide 2
 Satellite radiated power,
 RF spectrum,
 Connectivity,
 Adaptability to traffic and network growth,
 Handling of different types of traffic,
 Economics,
 Ground station complexity,
 Secrecy for some applications.
4.2 Multiplexing
Whenever the bandwidth of a medium linking two devices is greater than the bandwidth needs of the devices, the link can be shared. Multiplexing is the set of techniques that allows the (simultaneous) transmission of multiple signals across a single data link. As data and telecommunications use increases, so does traffic.

## Slide 3
Figure 4.1 multiplexing
4.3 Multiple Access
Multiple users want to communicate in common geographic area. Share the resources so that as many user as possible can communicate simultaneously without degradation in the performance of the system. Many people want to talk on their cell phones. Each phone must communicate with a base station.

## Slide 4
The Most Important Access Utilization Schemes (Techniques):
FDMA (Frequency Division Multiple Access)
TDMA (Time Division Multiple Access)
CDMA (Coded Division Multiple Access)
4.2 Frequency Division Multiple Access (FDMA)
FDMA is one of the earliest multiple-access techniques for cellular systems when continuous transmission is required for analog services. In this technique the bandwidth is divided into a number of channels and distributed among users with a finite portion of bandwidth for permanent use as illustrated in figure 4.2.

## Slide 5
Figure 4.2 Channel usages by FDMA
The FDMA operation is illustrated as follows
a. Given Radio Spectrum (RF BW) is divided into a large number of narrow-band radio channels called sub-divisions
b. Each sub-division has its own sub-carrier called IF Carrier
c. A control mechanism is required to ensure that each user/earth station uses only its own assigned sub-division at any time
d. Guard bands are used to prevent interference on the receiving end of the signal

## Slide 6
FDMA allocates a specific carrier frequency to a communication channel. The number of different users is limited to the number of "slices" in the frequency spectrum (Figure 5.3 ).
Figure 4.3 Carrier-frequency allocations among different users in a FDMA system.

## Slide 7
4.2.1 FDMA-Applications
FDMA is used in a variety of applications such as: telephone systems, radio systems, cable TV at homes.
The first generation of Mobile networks. FD,TD-MA.
GSM (Global System of Mobile Telecommunication) uses FDMA in combination with TDMA.
UMTS (Universal Mobile Telecommunication Systems-3G) in combination with other multiplexing techniques
4.3 FDMA may be divided into two main categories:
1. Multiple channel per carrier (MCPC)
2. Single channel per carrier (SCPC)

## Slide 8
 SCPC- a system where each sub-division carries only one 4-kHz voice channel
 MCPC-a system where several speech/voice band channels are frequency-division multiplexed to form a group, super-group or even master-group
The previous example is for MCPC system.
Baseband filter in earth station receiver corresponds to a specific transmitting station. Any change in traffic requires the retuning of this filter.
When traffic is low, e.g. service to remote areas, MCPC becomes wasteful of bandwidth because most of the channels remain unutilized for a significant part of the time. SCPC is used in this case.
In SCPC, each carrier transmits a single channel. SCPC may be pre-assigned
or demand-assigned. Pre-assigned e.g. 5 – 10 channels are permanently assigned to an earth station.

## Slide 9
4.4 Basic concept of FDMA in satellite communication
FDMA was the first multiple access technique employed in satellite communications. Because of its simplicity and flexibility, it remains very commonly used. In FDMA, a different frequency is allocated in a transponder to each carrier (possibly multi-destination) to be transmitted by an earth station, and then a given bandwidth, in proportion with the carrier capacity, is also allocated.
Figure 4.4 illustrates the basic concept of FDMA in satellite communications.
Different Earth stations are capable of selecting the carrier frequency containing messages of their interest.

## Slide 10
Two FDMA techniques are in operation today. One of them is the multichannel per carrier (MCPC) technique, where the Earth station frequency multiplexes several channels into one carrier base band assembly, which then frequency modulates an RF carrier and transmits it to an FDMA satellite transponder. In the other technique, called the single channel per carrier (SCPC), each signal channel modulates a separate RF carrier, which is then transmitted to the FDMA transponder. The modulation
technique used here could either be frequency modulation (FM) in case of analogue transmission or phase shift keying (PSK) for digital transmission.

## Slide 11
Figure 4.4 Basic concept of FDMA

## Slide 12
4.5 Principles of FDMA
Principles of FDMA are explained with the help of a communications
route between two earth stations A and B.
The bandwidth BT is divided into n segments which are assigned to all n
earth stations in the network according to their traffic requirements. The
FDMA scheme is shown in figure 4.5.
Fig (4.5)

## Slide 13
A communication route between two earth stations (A and B) in the network is shown in the figure (4.6).

## Slide 14
Fig(4.6)