## Slide 1
4.6 Time Division Multiple Access (TDMA)
TDMA is a digital technique that divides a single channel or band into time slots. Each time slot is used to transmit one byte or another digital segment of each signal in sequential serial data format. This technique works well with slow voice data signals, but it’s also useful for compressed video and other high-speed data.
TDMA requires careful time synchronization since users share the bandwidth in the frequency domain. This is illustrated in figure 5.6. Since the number of channels are less, inter channel interference is almost negligible, hence the guard time between the channels is considerably smaller

## Slide 2
Guard time is a spacing in time between the TDMA bursts. In cellular communications, when a user moves from one cell to another there is a chance that user could experience a call loss if there are no free time slots available. TDMA uses different time slots for transmission and reception. This type of duplexing is referred to as Time division duplexing (TDD). TDD does not require duplexers.
Figure 4.6 Channel usage by TDMA

## Slide 3
Time Division means that the frequency is divided up into blocks of time and only certain logical channels are transmitted at certain times. The time divisions in TDMA are known as Time Slots.
4.6.1 Time Slots
A frequency is divided up into 8 time slots, numbered 0 to 7.
Time Slots

## Slide 4
On a side note, also remember that GSM carrier frequencies are separated by 200kHz and that GSM operates in duplex. A channel number assigned to a pair of frequencies, one uplink and one downlink, is known as an Absolute Radio Frequency Channel Number (ARFCN Each time slot lasts 576.9 µs. A time slot is the basic radio resource used to facilitate communication between the MS and the BTS.
Time Slot Duration

## Slide 5
4.3.2 Data Rates
As stated earlier, GSM uses Gaussian Minimum-Shift Keying (GMSK) as its modulation method. GMSK provides a modulation rate of 270.833 kilobits per second (kb/s). At that rate, a maximum of 156.25 bits can be transmitted in each time slot (576.9 µs).
270.833 kb/s × 1000 = 270,833 bits/sec (Converting from kilobits to bits) 270,833 b/sec ÷ 1,000,000 = .207833 b/µs (Calculating bits per microsecond)
.207833 b/µs × 576.9 µs = 156.25 bits (Calculating number of bits per time
slot) So, 156.25 bits can be transmitted in a single time slot

## Slide 6
Bits per Time Slot
4.3.3 Data Burst
The data transmitted during a single time slot is known as a burst. Each burst allows 8.25 bits for guard time within a time slot. This is to prevent bursts from overlapping and interfering with transmissions in other time slots. Subtracting this from the 156.25 bits, there are 148 bits usable for each burst.

## Slide 7
a. Normal Burst
The data transmitted during a single time slot is known as a burst. Each burst allows 8.25 bits for guard time. This is to prevent bursts from overlapping and interfering with transmissions in other time slots. Out of 156.25, this leaves 148 bits usable for each burst.
b. Synchronization Burst
This burst is used for time synchronization of the mobile. The data payload carries the TDMA Frame Number (FN) and the Base Station Identity Code (BSIC). It is broadcast with the frequency correction burst. The Synchronization Burst is broadcast on the Synchronization Channel (SCH).

## Slide 8
4.4 FDMA + TDMA
A combination of FDMA/TDMA can be used. For example, in GSM systems. The traffic is burst onto the channel at a specific periods.
With this combination, more channels can be used with less interference.
FDMA and TDMA – A Comparison
In TDMA, only one carrier from any of several Earth Stations is
present at Satellite at any time
FDMA requires each Earth Station capable of transmitting and
receiving on multitude of carrier frequencies (FDMA/DAMA)
TDMA is more amenable to digital transmission (storage,
processing, rate-conversion etc.) than FDMA
TDMA requires precise synchronization

## Slide 9
With TDMA the different users speak and listen to each other according to a defined allocation of time slots (Figure 4.7). Different communication channels can then be established for a unique carrier frequency. Examples of TDMA are GSM,DECT, TETRA, and IS-136.
Figure 4.7. Time-slot allocations among different users in a TDMA system.

## Slide 10
Example :
• GSM is a TDMA/FDD system that uses 25 MHz for the forward link, with channels of 200 KHz. If 8 speech channels are supported on a single radio channel, and if no guard band is assumed, find the number of simultaneous users that can be accommodated in GSM.

## Slide 11
4.4 TDMA Frame Structure
As mentioned in fig (4.8), in a TDMA network, each of the multiple Earth stations accessing a given satellite transponder transmits one or more data bursts. The satellite thus receives at its input a set of bursts from a large number of Earth stations. This set of bursts from various Earth stations is called the TDMA frame.

## Slide 12
Fig (4.8)
Figure 4.9 shows a typical TDMA frame structure. It is evident from the frame structure that the frame starts with a reference burst transmitted from a reference station in the network. The reference burst is followed by traffic bursts from various Earth stations with a guard time between various traffic bursts from different stations.
The traffic bursts are synchronized to the reference burst to fix their timing reference.

## Slide 13
Fig 4.9

## Slide 14
4.4.1 Reference Burst
The reference burst is usually a combination of two reference bursts (RB1 and RB-2). The primary reference burst, which can be either RB-1 or RB-2, is transmitted by one of the stations, called the primary reference station, in the network. The reference burst does not carry any traffic information and is used to provide timing references to various stations accessing the TDMA transponder.
4.4.2 Traffic Burst
Different stations accessing the satellite transponder may transmit one or more traffic bursts per TDMA frame and position them anywhere in the frame according to a burst

## Slide 15
time plan that coordinates traffic between various stations. The reference burst also provides timing references to the stations for transmitting their traffic bursts so as to ensure that they arrive at the satellite transponder within their designated positions in the TDMA frame.
4.4.3 Guard Time
Different bursts are separated from each other by a short guard time, which ensures that the bursts from different stations accessing the satellite transponder do not overlap.
4.5.4 Traffic Information
Traffic bursts follow the reference burst in the TDMA frame structure. Each station in the TDMA network can transmit and receive many traffic bursts and sub-bursts per frame. The length of each sub-burst, which represents information on a certain channel, depends upon the type of service and the number of channels being supported in the traffic burst.