## Slide 1
Chapter 3
GSM system overview
3.1 Introduction:
GSM (Global System for Mobile communications: originally from Groupe Spécial Mobile) is the most popular standard for mobile phones in the world. GSM networks operate in a number of different frequency ranges (separated into GSM frequency ranges for 2G and UMTS frequency bands for 3G). Most 2G GSM networks operate in the 900 MHz or 1800 MHz bands. Some countries in the Americas (including Canada and the United States) use the 850 MHz and 1900 MHz bands because the 900 and 1800 MHz frequency bands were already allocated. Most 3G GSM networks in Europe operate in the 2100 MHz frequency band.
GSM-900 uses 890–915 MHz to send information from the mobile station to the base station (uplink) and 935–960 MHz for the other direction (downlink), providing 125 RF channels (channel numbers 0 to 124) spaced at 200 kHz. Duplex spacing of 45 MHz is used.

## Slide 2
Example
The global system for mobile communications (GSM) utilizes the frequency band 935–960 MHz for the forward link and frequency range 890–915 MHz for the reverse link. Each 25-MHz band is broken into radio channels of 200 kHz. Each radio channel consists of eight time slots. If no guard band is assumed, ﬁnd the number of simultaneous users that can be accommodated in GSM. How many users can be accommodated if a guard band of 100 kHz is provided at the upper and the lower end of the GSM spectrum?
Solution
The number of simultaneous users that can be accommodated in GSM in the ﬁrst case is equal to
In the second case the number of simultaneous users is equal to 992.

## Slide 3
3.2 GSM architecture:
AGSM network is made up of three subsystems as shown in fig(3.1) :
a.The Mobile Station (MS)
b.The Base Station Sub-system (BSS) – comprising a BSC and several BTSs
c.The Network and Switching Sub-system (NSS) – comprising an MSC and
associated registers
Several interfaces are defined between different parts of the system:
• 'A' interface between MSC and BSC
• 'Abis' interface between BSC and BTS
• 'Um' air interface between the BTS (antenna) and the MS

## Slide 4
Fig(3.1) GSM architecture

## Slide 5
Abbreviations:
MSC – Mobile Switching Centre BSS – Base Station Sub-system
BSC – Base Station Controller HLR – Home Location Register
BTS – Base Transceiver Station VLR – Visitor Location Register
TRX – Transceiver AuC – Authentication Centre
MS – Mobile Station EIR – Equipment Identity Register
OMC – Operations and Maintenance Centre
PSTN – Public Switched Telephone Network

## Slide 6
3.2.1 Mobile Station
The mobile station consists of:
a• mobile equipment (ME)
b• subscriber identity module (SIM)
The SIM stores permanent and temporary data about the mobile, the subscriber and the network, including:
• The International Mobile Subscribers Identity (IMSI)
• MS ISDN number of subscriber
• Authentication key (Ki) and algorithms for authentication check
• The mobile equipment has a unique International Mobile
Equipment Identity (IMEI), which is used by the EIR

## Slide 7
One of the key features of GSM is the Subscriber Identity Module, commonly known as a SIM card. The SIM is a detachable smart card containing the user's subscription information and phone book. This allows the user to retain his or her information after switching handsets. Alternatively, the user can also change operators while retaining the handset simply by changing the SIM. Some
3.2.2 Base Station System (BSS);
The BSS comprises:
• Base Transceiver Station (BTS)
• One or more Base Station Controllers (BSC)
• The purpose of the BTS is to:
• provide radio access to the mobile stations
• manage the radio access aspects of the system

## Slide 8
• BTS contains:
• Radio Transmitter/Receiver (TRX)
• Signal processing and control equipment
• Antennas and feeder cables
• The BSC:
• allocates a channel for the duration of a call
• maintains the call:
• monitoring quality
• controlling the power transmitted by the BTS or MS
• generating a handover to another cell when required

## Slide 9
The effect of gains and losses in the BTS equipment on the signal power sent to the antenna is an important consideration for link budget calculations.

## Slide 10
3.2.3 Network Switching system (NSS);