## Slide 1
2.4 Generation of cellular system
2.4 .1 First Generation (1G)
(1G) The first generation cellular systems that introduced in the 1980s generally employ analog Frequency Modulation (FM) techniques. The Advanced Mobile Phone System (AMPS) is the most notable of the first generation systems.
The main technology of this first generation mobile system was FDMA/FDD and analog FM.
First-generation systems suffered from :
limitations such as low service quality,
long call setup time,
inefficient use of bandwidth,
susceptibility to interference,
bulky and expensive equipment’s and only support for speech.
All the first generation cellular systems employ Frequency Division Multiple Access (FDMA) to carry analog voice over channels in the 800 MHz frequency band.

## Slide 2
2.4 .2 Second Generation - 2G
The rapid growth in the number of subscribers , second generation cellular systems introduced in the 1990s and take the advantage of compression and coding techniques associated with digital technology. All the second generation systems employ digital modulation were introduced in this generation with the main technology as TDMA/FDD and CDMA/FDD.
The specification of 2G:
1-Digital data can be compressed and multiplexed much more effectively than analog voice encodings.
2-Multiplexing -multiple analog message signals or digital data streams are combined into one signal.

## Slide 3
3-Allows for lower powered radio signals that require less battery power.
4-Digital voice data can be compressed and multiplexed much more effectively than analog.
5- CODEC introduction -program that encodes and decodes digital data stream or signal.
6-Translates data from digital to analog and vice .

## Slide 4
Second-generation cellular systems support:
Data, speech and facsimile services.
The systems use encryption mechanisms to protect data and speech.
use advance mobility management and support power control.
The 2G systems introduced three popular TDMA standards and one popular CDMA standard in the market. These are:
a.TDMA/FDD Standards
1.Global System for Mobile (GSM): The GSM standard, introduced by Groupe Special Mobile, was aimed at designing a uniform pan-European mobile system. It was the first fully digital system utilizing the 900 MHz frequency band. The initial GSM had 200 KHz radio channels, encryption of speech, low speed data services and support for SMS for which it gained quick popularity.

## Slide 5
2.Interim Standard 136 (IS-136): The need of this system was mainly to increase the capacity over the earlier analog (AMPS) system.
b. Pacific Digital Cellular (PDC): This standard was developed as the counterpart of NADC in Japan. The main advantage of this standard was its low transmission bit rate which led to its better spectrum utilization.
c..CDMA/FDD Standard known as CDMA- One
These systems provide better service quality than those of the first-generation cellular systems and use bandwidth more efficiently.
Differences between First and Second Generation Systems:
1.Digital traffic channels – first-generation systems are almost purely analog; second-generation systems are digital

## Slide 6
2.Encryption – all second generation systems provide encryption to prevent eavesdropping
3.Error detection and correction – second-generation digital traffic allows for detection and correction, giving clear voice reception Channel access – second-generation systems allow channels to be dynamically shared by a number of users
2.5 G (GPRS) [The General Packet Radio Service]
is used to describe 2G-systems that have implemented a packet-switched domain . Extends the capabilities of 2G systems by providing additional features, such as a packet-switched connection(GPRS) in the TDMA-based GSM system, and enhanced data rates .
GPRS could provide data rates from 56 kbit/s up to 115 kbit/s. It can be used for services such as Wireless Application Protocol (WAP) access, Multimedia Messaging , Service (MMS), and for Internet communication services such as email and World Wide Web access.

## Slide 7
2.4.3 Third Generation - 3G
3G technology came along to support increased data needs. 3G stands for "third generation" -- this makes analog cellular technology generation one and digital/PCS generation two. 3G technology is intended for the true multimedia cell phone -- typically called smartphones -- and features increased bandwidth and transfer rates to accommodate Web-based applications and phone-based audio and video files.
The specification of 3G:
1-Large capacity and broadband capabilities. •Allows the transmission of 384kbps for mobile systems and up to 2Mbps.
2-Increased spectrum efficiency –5Mhz–
-A greater number of users that can be simultaneously supported by a radio frequency bandwidth.
3-High data rates at lower incremental cost than 2G.
4-Global roaming
5-CDMA –Code Division Multiple Access.

## Slide 8
2.4.4 Fourth generation 4G
The fourth generation mobile communication system is developed after the third generation (3G) mobile phone standards.
The features included in 4G are Video conferencing, gaming services, IP telephony, high definition (HD) mobile TV. It also provides Internet access facility at a very rapid speed which is known as mobile ultra-broadband internet access.
Features of 4G:
•Faster and more reliable. 100 Mb/s (802.11g wireless = 54Mb/s, 3G = 2Mb/s)
•Lower cost than previous generations
•Multi-standard wireless system.
–Bluetooth, Wired, Wireless (802.11x)
•Ad Hoc Networking.
•OFDM used instead of CDMA.
•Potentially IEEE standard 802.11n
–Most information is proprietary.

## Slide 9
2.5 How Cellular Telephones Work
Mobile phones work by sending and receiving low power radio signals, much like a 2 way radio system. The signals are sent to and received from antennas that are attached to radio transmitters and receivers, commonly referred to as mobile phone base stations. The base stations are linked to the rest of the mobile and fixed phone network and pass the signal/call on into those networks.
This allows extensive frequency reuse across a city, so that millions of people can use cell phones simultaneously.
In a typical analog cell-phone system in the United States, the cell-phone carrier receives about 800 frequencies to use across the city. The carrier chops up the city into cells. Each cell is typically sized at about 10 square miles (26 square kilometers). Cells are normally thought of as hexagons on a big hexagonal grid, as shown in fig (2.5 )

## Slide 10
Fig(2.5 )
Because cell phones and base stations use low-power transmitters, the same frequencies can be reused in non-adjacent cells. A single cell in an analog system uses one-seventh of the available duplex voice channels. That is, each cell (of the seven on a hexagonal grid) is using one-seventh of the available channels so it has a unique set of frequencies and there are no collisions:
A cell-phone carrier typically gets 832 radio frequencies to use in a city.
Each cell phone uses two frequencies per call – a duplex channel – so there are typically 395 voice channels per carrier. (The other 42 frequencies are used for control channels .)

## Slide 11
Therefore, each cell has about 56 voice channels available.
In other words, in any cell, 56 people can be talking on their cell phone at one time. With digital transmission methods, the number of available channels increases. For example, a TDMA-based digital system can carry three times as many calls as an analog system, so each cell has about 168 channels available.
Cell phones have low-power transmitters in them. Many cell phones have two signal strengths: 0.6 watts and 3 watts (for comparison, most CB radios transmit at 4 watts). The base station is also transmitting at low power.
Each carrier in each city also runs one central office called the Mobile Telephone Switching Office (MTSO). This office handles all of the phone connections to the normal land-based phone system, and controls all of the base stations in the region

## Slide 12
.
2.6 Cell Phone Codes All cell phones have special codes associated with them. These codes are used to identify the phone, the phone’s owner and the service provider.
The Cell Phone Codes are as following:
- Electronic Serial Number (ESN) – a unique 32-bit number programmed into the phone when it is manufactured - Mobile Identification Number (MIN) – a 10-digit number derived from your phone’s number - System Identification Code (SID) – a unique 5-digit number that is assigned to each carrier by the FCC
While the ESN is considered a permanent part of the phone, both the MIN and SID codes are programmed into the phone when you purchase a service plan and have the phone activated