## Slide 1
Cell Cluster:
Considering a cellular system that has a total of S duplex radio channels. If each cell is allocated a group of k channels (k < S)and if the S channels are divided among N cellsinto unique and disjoint channel groups of same number of channels, then,
S = kN
The N cells that collectively use the complete set of available frequencies is called a cluster. If a cluster is replicated M times within the system, the total number of duplex channels or capacity,
C = MkN = MS
• Total available channels = S
• N “adjacent” cells (called a cluster) share S channels
• System has M clusters

## Slide 2
Each cell gets k channels S = k N
Capacity of the system is C = MkN
Frequency reuse factor is 1/ N

## Slide 3
The capacity is directly proportional to M. The factor N is called the cluster size and is typically 4, 7 or 12. If the cluster size N is reduced while the cell size is kept constant, more clusters are required to cover a given area and hence more capacity is achieved from the design viewpoint, the smallest possible value of N is desirable to maximize capacity over a given coverage area. The frequency reuse factor of a cellular system is 1/ N, since each cell within a cluster is assigned 1/N of the total available channels in the system.
In this example,
The cluster size N = 7 and the frequency reuse factor is 1/7 since each cell contains one-seventh of the total number of available channels.

## Slide 4
Example1:
Compute total system capacity
• of cells = 262.4/2.6=100 cells
• of usable duplex channels/cell
– S=( of channels)/(reuse factor)
– S4=1000/4=250
– S7=1000/7=142

## Slide 5
• Total system capacity ( of users could be accommodated simultaneously)
– C=S*( cells)
– C4=250*100=25000
– C7=142*100=14200
Example 2
949 – 900 = 49 MHz the bandwidth
49 / 7 = 7 MHz / cell

## Slide 7
Example 3
Let a total of 33MHz of bandwidth be allocated to a particular FDD cellular telephone system, which uses two 25kHz simplex channels to provide full duplex voice and control channels. Compute the number of channels available
per cell if the system uses (a) 4-cell reuse, (b) 7-cell reuse, and (c) 12-cell reuse. If 1 MHz of the allocated spectrum is dedicated to control channels, determine an equitable distribution of control channels and voice
channels in each cell for each of the three systems.
Solution
Given: Total bandwidth = 33 MHz.
Channel bandwidth = 25 kHz simplex channels. 25x2 = 50 kHz duplex channels.
Total available channels = 33,000/50 = 660 channels.
(a) for N = 4, total number of channels available per cell = 660/4
≈ 165 channels.
(b) for N = 7, total number of channels available per cell = 660/7 ≈ 95 channels.
(c) for N = 12, total number of channels available per cell = 660/12
≈ 55 channels.

## Slide 8
A 1 MHz spectrum for control channels implies that there are 1000/50 = 20 control channels out of the 660 channels available. To evenly distribute the control and voice channels, simply allocate the same number of channels in each cell wherever possible. Here, the 660 channels must be evenly distributed to each cell within the cluster. In practice, only the 640 voice channels would be allocated, since the control channels are allocated separately as 1 per cell.
a. For N = 4, we can have 5 control channels and 160 voice channels per cell. In practice, however, each cell only needs a single control channel (the control channels have a greater reuse distance than the voice
channels). Thus, one control channel and 160 voice channels would be assigned to each cell.
b. For N = 7, 4 cells with 3 control channels and 92 voice channels, 2 cells with 3 control channels and 90 voice channels, and 1 cell with 2 control channels and 92 voice channels could be allocated. In practice, however, each cell would have one control channel, four cells would have 91 voice channels, and three cells would have 92 voice channels.

## Slide 9
For N = 12, we can have 8 cells with 2 control channels and 53 voice channels, and four cells with 1 control channel and 54 voice channels each. In an actual system, each cell would have 1 control channel, 8 cells would have 53 voice channels, and 4 cells would have 54 voice channels.
example 4
The American analog technology standard, known as Advanced Mobile Phone
Service (AMPS), employs frequency modulation and occupies a 30-kHz frequency slot for each voice channel [47]. Suppose that a total of 25-MHz bandwidth is allocated to a particular cellular radio communication system with cluster size 7. How many channels per cell does the system provide?
Solution
Allocation of 12.5 MHz each for forward and reverse links provides a little more
than 400 channels in each direction for the total system, and correspondingly a
little less than 60 per cell.

## Slide 10
2.10. Handover
When a mobile unit moves from one cell to another it moves into a region with a completely new set of frequencies. Initially such activity resulted in the loss of the call. In order to avoid losing calls a procedure termed handover was introduced. In GSM, the mobile station continuously monitors the perceived power levels of the serving cell and the neighboring cells. If the power levels indicate that the power level of an adjacent cell is more than that of the current cell a handover is performed. The handover allows the mobile unit to communicate with the base station of the new cell with new set of frequencies. Depending on the two cells in question, the handover can be between two sectors with the same base station, between two BSCs, between two MSCs belonging to the same operator or even between two networks . The concept of handover is illustrated in Figure (2.11).

## Slide 11
Fig(2.11)