## Slide 1
MOBILE COMMUNICATION
الاتصالات المحمولة
(Chapter one)
د. عمانوئيل سليم

## Slide 2
Chapter one
Mobile wireless communication system
1.1 Basics of Communication Network
Telecommunications is the communicative technology of transmitting signals in the forms of voice, information, image, etc., which can be characterized into two types:
• Fixed-line Communication Networks, including basic telephone, international telephone, public telephone and internet, etc.
• Wireless Communication Networks, including mobile phone, paging and trunked mobile, etc.
A wireless communication link includes a transmitter, a receiver, and a channel. Quantization, coding and decoding are only performed in digital systems. Most links are full duplex and include a transmitter and a receiver or a transceiver at each end of the link.

## Slide 3
In a mobile communication system at least one of the transceivers is mobile. Basic types of systems include base/mobile, peer-to-peer, repeater, and mobile satellite systems. In a base/mobile system, a base station connected to a public network communicates with a mobile unit. This gives the mobile unit access to the public network. Cellular telephony uses the base/mobile configuration to give mobile users access to the public switched telephone network, as shown in Fig (1.1) (a). In peer-to-peer systems, mobile units communicate directly with each other. Mobile units sharing a frequency channel can communicate with one another, as shown in Fig(1.1) (b).
Fig (1.1) (c) shows a repeater system. In this system, all users transmit on one channel and listen on a second channel. In a mobile satellite system, one or more satellites relays signals between a mobile user and an earth-based base
station or “gateway” that connects to the public switched , as shown in Fig (1. 1) (d).

## Slide 4
Figure(1.1). mobile radio systems: a) mobile/base, b) peer-to-peer, c)repeater,d) mobile satellite
Example of Mobile Radio Systems
– Cordless phone – Remote controller – Hand-held walkie-talkies
– Pagers – Cellular telephone -- Wireless LAN

## Slide 5
1.2 Radio Transmission Techniques
Based on the type of channels being utilized, mobile radio transmission systems may be classified as the following three categories.
1.2.1 One-Way(simplex) Radio Communication
Simplex is the simplest type of radio communication. In simplex communication, there is a one-way communication between the sender or transmitter and the receiver as shown in fig(1.2). Simplex communications is nowadays mostly limited to broadcast applications.
Figure 1.2: Simplex Radio System

## Slide 6
1.2.2 Half Duplex Communication
In half-duplex radio, both transmitters use the same frequency. Only one party can talk at a time. The same channel is used for both transmit and receive directions of transmission and simply shared over time as shown in fig (1.3).
fig (1.3).
1.2.3 Two-Way (full duplex) Radio Communication
In full-duplex radio, the two transmitters use different frequencies, so both parties can talk at the same time Cell phones are full-duplex.
It requires two transmitters and two receivers, one transmitter and one receiver at both of the communication link as shown in fig 1.4

## Slide 7
Figure 1.4: Full Duplex Radio System
This is possible by one of the two following methods:
a. Frequency Division Duplexing (FDD):
FDD supports two-way radio communication by using two distinct radio channels. One frequency channel is transmitted downstream from the BS to the MS (forward channel). A second frequency is used in the upstream direction and supports transmission from the MS to the BS (reverse channel).

## Slide 8
b. Time Division Duplexing (TDD):
TDD uses a single frequency band to transmit signals in both the downstream and upstream directions. TDD operates by toggling transmission directions over a time interval. This toggling takes place very rapidly and is imperceptible to the user.
Figure 1.5: (a) Frequency division duplexing and (b) time division duplexing.

## Slide 9
1.3 Cellular mobile radio systems
A cellular radio system provides a wireless connection to the public telephone network for any user location within the radio range of the system. The term mobile has traditionally been used to classify a radio terminal that can be moved during communication. Cellular systems accommodate a large number of mobile units over a large area within a limited frequency spectrum. There are several types of radio transmission systems. We consider only full duplex systems. These are communication systems that allow simultaneous two-way communication. Transmission and reception for a full duplex system are typically on two different channels, so the user may constantly transmit while receiving signals from another user.
Other examples of radio communication applications include paging, amateur radio, dispatch, citizens band (CB), public service, cordless phones, and terrestrial microwave radio systems.
1.3.1 The basic idea of cell mobile communication
A good way to understand the sophistication of a cell mobile (phone) is to compare it to a CB radio or a walkie-talkie.

## Slide 10
a.Full-duplex vs. half-duplex
Both walkie-talkies and CB radios are half-duplex devices. That is, two people communicating on a CB radio use the same frequency, so only one person can talk at a time. A cell phone is a full-duplex device. That means that you use one frequency for talking and a second, separate frequency for listening. Both people on the call can talk at once.
b.Channels -
A walkie-talkie typically has one channel, and a CB radio has 40 channels. A typical cell phone can communicate on 1,664 channels or more!
c.Range –
A walkie-talkie can transmit about 1 mile (1.6 km) using a 0.25-watt transmitter. A CB radio, because it has much higher power, can transmit about 5 miles (8 km) using a 5-watt transmitter. Cell phones operate within cells, and they can switch cells as they move around. Cells give cell phones incredible range.
Full duplex half duplex
Fig 1.6

## Slide 11
1.4 paging system:
Pager (sometimes called a page, beeper, bleep or bleeper)
Paging systems are communication systems that send brief messages to a subscriber. Depending on the type of service, the message may be either a numeric message, an alphanumeric message, or a voice message. Paging systems are typically used to notify a subscriber of the need to call a particular telephone number or travel to a known location to receive further instructions. In modern paging systems, news headlines, stock quotations, and faxes may be sent. A message is sent to a paging subscriber via the paging system access number (usually a toll-free telephone number) with a telephone keypad or modem. The issued message is called a page. The paging system then transmits the page throughout the service area using base stations which broadcast the page on a radio carrier.

## Slide 12
Fig(1.7)
Paging systems vary widely in their complexity and coverage area. While simple paging systems may cover a limited range of 2 to 5 km, or may even be confined to within individual buildings, wide area paging systems can provide worldwide coverage. Figure(1.7) shows a diagram of a wide area paging system. The paging control center dispatches pages received from the PSTN throughout several cities at the same time