## Slide 2
3.3 GSM Frequency Allocation
There are two frequency bands of 25 MHz each that have been allocated for
the use of GSM. The band 890 - 915 MHz is used for the uplink direction (from the mobile station to the base station). The band 935 - 960 MHz is used for the downlink direction (from the base station to the mobile station)
GSM Frequency Bands
GSM uses TDMA within a FDMA structure. As a result, different users can
transmit using the same frequency, but they can't transmit at the same time.

## Slide 3
A 25MHz frequency band is divided using an FDMA scheme into 124 one- way carrier frequencies. Each base station is assigned one or more carriers to use in its cell. A 200kHz frequency band separates the carrier frequencies from each other. Normally, a 25MHz band should be divisible into 125 carrier frequencies but in GSM the 1st carrier frequency is used as a guard band between GSM and other services that might be working on lower frequencies
3.4 GSM security
In any mobile system it important to send or receive or any kind of data in security situation, it's important to reach to the services in any time, it's also important to not any one to use other accounts. All these threats require good security in the mobile system. The GSM designed to be secure mobile phone system with strong subscriber authentication and over the air transmission encryption. The security model and algorithms were developed in secrecy and

## Slide 4
were never published. Eventually some of the algorithms and specification are leaked out.
GSM uses several cryptographic algorithms for security. The A5/1 and A5/2 stream ciphers are used for ensuring over-the-air voice privacy. A5/1 was developed first and is a stronger algorithm used within Europe and the United States; A5/2 is weaker and used in other countries.
The key generation algorithm used in the GSM system is known as the A8 algorithm.

## Slide 5
A8's task is to generate the 64-bit Session Key (Kc), from the 128-bit random challenge (RAND) received from the Mobile Services Switching Center (MSC) and from the 128-bit Individual Subscriber Authentication Key (Ki) from the Mobile Station's Subscriber Identity Module (SIM) or the Home Location Register (HLR).
One Session Key (Kc) is used until the MSC decides to authenticate the MS again. This might take days.
A8 actually generates 128 bits of output. The last 54 bits of those 128 bits form the Session Key (Kc). Ten zero-bits are appended to this key before it is given as input to the A5 algorithm.
The A8 algorithm is implemented in the Subscriber Identity Module (SIM).

## Slide 6
GSM security

## Slide 7
3.5 GSM Authentication
There is a secret authentication key Ki for each subscriber, which is stored in their SIM and in the AuC, but nowhere else. The AuC generates a random number (RAND) which is passed together with the key through an algorithm known as A3. This produces a signed result value (SRES). The values of RAND and SRES (but not the key) are passed to the MSC. The MSC sends RAND to the mobile, which uses its key and the A3 algorithm to generate SRES.
The MS returns its SRES value to the MSC, which compares the two values. If they are the same, the mobile is allowed on the network.
This system provides fairly good (but not perfect) protection against fraud and SIM cloning. It can however be broken
The A8 algorithm is used to generate a second key (Kc) which is used to apply encryption to the voice or data being transmitted. Again this provides limited protection against interception of the message.

## Slide 8
Fig (3.2) GSM Authentication

## Slide 9
3.6 GSM Burst Structure
The GSM uses both FDMA and TDMA for multiple access. GSM900 uses the 890 MHz to 960 MHz frequency band for communication. GSM900 has two frequency bands 45 MHz apart. The 890 MHz to 915 MHz frequency band is used for the uplink from a MS to a BS and the 935 MHz to 960 MHz frequency band is used for the downlink from a BS to a MS. Each of the two bands is subdivided into 124 single carrier channels of 200 KHz each. A guard band of 200 KHz is left on both sides of the uplink and the downlink bands.
GSM1800 uses the 1710 MHz to 1880 MHz frequency band for communication. Each carrier frequency is then divided according to time using a TDMA scheme. Each of the carrier frequencies is divided into a 120ms multiform. A multiform is made up of 26 frames. Two of these frames are used for control purposes, while the remaining 24 frames for traffic.

## Slide 10
Structure of a Multiframe

## Slide 11
Each frame can in turn be divided into 8 bursts, and each of the 8 bursts is
assigned to ta single user. In a TDMA system, a burst is the unit of time,
and each burst lasts for approximately 0.577 ms.
GSM1800 uses the 1710 MHz to 1880 MHz frequency band for communication . the burst structure of the uplink channel is presented in fig ( 3.4 ) and the frequency allocation for GSM900 and GSM 1800 is presented in fig ( 3.5 ) .
Fig(3.5) GSM900 and GSM 1800

## Slide 12
Each voice channel is digitized and compressed to a 13-Kbps digital signal. Each slot carries 156.25 bits. Eight slots are multiplexed together, creating a TDM frame.
Twenty-six frames are combined to form a multiframe. We can calculate the bit rate of each channel as follows:
Channel data rate= (1/120 ms) x 26x 8 x 156.25=270.8 Kbps
Each 270.8-Kbps digital channel modulates a carrier using
GMSK (a form of FSK used mainly in European systems); the result is a 200-KHz analog signal. Finally 124 analog channels of 200 KHz are multiplexed together using FDMA. The result is a 25-MHz band.

## Slide 13
Fig(3.6) GSM system using TDMA/FDMA network