## Slide 1
Chapter 2
Cellular network
2.1 Introduction :
A cellular network is a radio network made up of a number of radio cells (or just cells) each served by at least one fixed-location transceiver known as a cell site or base station. These cells cover different land areas to provide radio coverage over a wider area than the area of one cell, so that a variable number of portable transceivers can be used in any one cell and moved through more than one cell during transmission.
Cellular networks offer a number of advantages over alternative solutions:
increased capacity
reduced power usage
larger coverage area
reduced interference from other signals

## Slide 2
The most common example of a cellular network is a mobile phone (cell phone) network. A mobile phone is a portable telephone which receives or makes calls through a cell site (base station), or transmitting tower.
2.2 Cellular Network Organization
The first generation cellular system that is analogue works by organizing a group of adjoining cells, each cell is managed by a base station (BS). The base stations are connected to public switch telephone networks (PSTN) through the mobile switching centers (MSCs) by land links ( Mobile Telecommunications
Switching Office (MTSO)) see fig(2.1)
Fig (2.1) overview of cellular system

## Slide 3
2.2.1 the cellular network consists of:
a. Mobile station (MS): A device used for communication over the network.
b. Base station transceiver (BST): A transmitter/receiver used to Transmit / receive
signals over the network.
c. Mobile switching center (MSC): Sets up and maintains calls made over the network.
Base station controller (BSC): Communication between a group of BSTs and a
single MSC is controlled by the BSC
e. Public switched telephone network (PSTN): Section of the network that is
land base
Two types of channels available between mobile unit and BS:
Control channels used to exchange information having to do with setting up and maintaining calls (out-band or in-band through stealing bits)
b. Traffic channels :carry voice or data connection between users

## Slide 4
    2.2.3 Cellular telephone system
Wireless telephones come in two basic varieties: cordless phones and mobile phones (sometimes called cell phones).
a. Cordless phones are devices consisting of a base station and a handset sold as a set for use within the home.
• Two-way (duplex) communications
• Consists of a portable handset, connected to dedicated base station, which is connected to the telephone network

## Slide 5
Mobile phones have gone through three distinct generations, with different technologies:
1. Analog voice.
2.Digital voice.
3.Digital voice and data (Internet, e-mail, etc.).
• Characteristic
– Large number of users
– Large Geographic area
– Limited frequency spectrum
– Reuse of the radio frequency by the concept of “cell’’.
2.2.4 Mobile Telephone Switching Office (MTSO)
The MTSO is the central office for mobile switching. It houses the mobile switching center (MSC), field monitoring, and relay stations for switching calls from cell sites to wire line central offices (PSTN). In analog cellular networks, the MSC controls the system operation. The MSC controls calls, tracks billing information, and locates cellular subscribers.

## Slide 6
2.2.5 PSTN
The public switched telephone network (PSTN) is the network of the world's public circuit-switched telephone networks. It consists of telephone lines, fiber optic cables, microwave transmission links, cellular networks, communications satellites, and undersea telephone cables, all inter-connected by switching centers, thus allowing any telephone in the world to communicate with any other. Originally a network of fixed-line analog telephone systems, the PSTN is now almost entirely digital in its core and includes mobile as well as fixed telephones
2.2.4 Operational Channels
In each cell, there are four types of channels that take active part during a mobile call. i.e Communication between the base station and mobiles is defined by the standard common air interface (CAI) These are:

## Slide 7
–forward voice channel (FVC): voice transmission from base station to mobile
–reverse voice channel (RVC): voice transmission from mobile to base station
–forward control channels (FCC): initiating mobile call from base station to mobile
–reverse control channel (RCC): initiating mobile call from mobile to base station
Fig2.3.

## Slide 8
2 .3 Cellular Access Technologies
There are three common technologies used by cell-phone networks for transmitting information:
Frequency division multiple access (FDMA)
Time division multiple access (TDMA)
Code division multiple access (CDMA)
The first word tells you what the access method is. The second word, division, lets you know that it splits calls based on that access method.
FDMA puts each call on a separate frequency.
TDMA assigns each call a certain portion of time on a designated frequency.
CDMA gives a unique code to each call and spreads it over the available frequencies.
The last part of each name is multiple access. This simply means that more than one user can utilize each cell.